## Slide 1: CoAP Protocol Negotiation draft-silverajan-core-coap-protocol-negotiation Bill Silverajan TUT Mert Ocak Ericsson

## Slide 2: Background
Currently at draft version -07
Aimed at CoAP nodes that have multiple transports, and wish to allow CoAP requests and responses over some or all these transports
Allows clients to directly query origin servers for available transports and communicate using an alternative transport
When a CoRE Resource Directory is present, origin servers can also register transport availability to RD for clients to query
Both per-server and per-resource models supported

## Slide 3: Allow Discovery
CoAP clients to discover active transports on an origin server
R1
Type T1
CoAP Server
SMS
UDP
Type T2
CoAP Client
UDP
SMS
Can I get resources over UDP?
Radio’s up, yes you can, here’s how
CoAP GET Request for R1
CoAP Response

## Slide 4: Better caching
Express same/related resource in alternate transports and locations
Type T2
CoAP Server
UDP
TCP
HTTP Client A
HTTP
HTTP Client B
HTTP
HTTP - CoAP Proxy
UDP
TCP
HTTP
R1
R1
R1 retrieved only once
coap/udp
coap/tcp
1. HTTP Client A to Proxy: Get me CoAP Server resource R1 over UDP
2. Proxy gets R1 from CoAP Server over UDP
3. HTTP Client B to Proxy: Get me CoAP Server resource R1 over TCP
4. Proxy to CoAP Server over UDP: Is it the same resource over TCP?
5. CoAP Server to Proxy over UDP: Yes, it is
6. Proxy Server returns cached R1 to HTTP Client B

## Slide 5: Protocol and Payload Extensions
A new CoAP Option called Alternative-Transport
  This enables clients to query for one or more available transports at an origin server for interacting with all resources
A new CoRE Link attribute called OL
  This enables an origin server to expose alternative transports on a per-resource basis

## Slide 6: CoAP Option: Alternative-Transport
Used bidirectionally between client and origin server
Flexible means to discover multiple transports
Functional equivalence to using an RD for transport discovery
+-----+---+---+---+---+------------------------+--------+--------+----------+
| No. | C | U | N | R | Name | Format | Length | Default |
+-----+---+---+---+---+------------------------+--------+--------+----------+
| 66 | | x | - | x | Alternative-Transport | string | 0-1034 | (none) |
+-----+---+---+---+---+------------------------+--------+--------+----------+
C=Critical, U=Unsafe, N=No-Cache-Key, R=Repeatable

## Slide 7: CoAP Option: Alternative-Transport
Client Server
| |
| GET /temperature |
| Token: 0x64 |
| Alternative-Transport: tcp |
+-------------------------------------->|
| |
| 2.05 Content |
| Token: 0x64 |
| Payload: 21.0 Cel |
| Alternative-Transport: |
| coap+tcp://server.example.org/ |
| Alternative-Transport: |
| coaps+tcp://server.example.org/ |
| |
|<--------------------------------------+
| |

## Slide 8: CoAP Option: Alternative-Transport
Client Server
| GET /temperature |
| Token: 0x64 |
| Alternative-Transport: tcp |
| Alternative-Transport: sms |
+-------------------------------------->|
| |
| 2.05 Content |
| Token: 0x64 |
| Payload: 21.0 Cel |
| Alternative-Transport: |
| coap+sms://0015105550101/ |
| Alternative-Transport: |
| coap+tcp://server.example.org/ |
| Alternative-Transport: |
| coaps+tcp://server.example.org/ |
| |
|<--------------------------------------+
| |

## Slide 9: CoAP Option: Alternative-Transport
Client Server
| GET /temperature |
| Token: 0x64 |
| Alternative-Transport: (null) |
+-------------------------------------->|
| |
| 2.05 Content |
| Token: 0x64 |
| Payload: 21.0 Cel |
| Alternative-Transport: |
| coap+sms://0015105550101/ |
| Alternative-Transport: |
| coap+tcp://server.example.org/ |
| Alternative-Transport: |
| coaps+tcp://server.example.org/ |
| Alternative-Transport: |
| coaps+ws://server.example.org/ |
| |
|<--------------------------------------+
| |

## Slide 10: Extensions to CoRE RD
Extend the Resource Directory’s Registration and Update Interfaces
  New optional ‘at’ RD parameter
Extend the Resource Directory’s Lookup Interface
  New optional ‘tt’ RD parameter

## Slide 11: Using CoRE RD: Advantages
RD provides well-defined interfaces with easy way to extend functionality
Consistent API: Registrations and Updates managed by origin servers based on lifetime values
Group function set provides new possibilities
Support for commissioning tools (via ‘con’)
RD also supports HTTP

## Slide 12: New ‘at’ RD parameter
Req: POST coap:/rd.example.com/rd?ep=node1&
at=coap+tcp://server.example.com
Content-Format: 40
Payload:
</sensors/temp>;ct=41;rt="temperature-f"; if="sensor",
</sensors/door>;ct=41;rt="door";if="sensor"
Res: 2.01 Created
Location: /rd/4521

## Slide 13: New ‘tt’ RD parameter
Req: GET /rd-lookup/ep?ep=node5&tt=*
Res: 2.05 Content
<coap+tcp://[FDFD::123]:61616>;ep="node5",
<coap+ws://[FDFD::123]:61616>;ep="node5"

## Slide 14: Example RD Registration and Lookups
Registration Request from origin server to RD
POST coap:/rd.example.org/rd?ep=node1
&at=coap+tcp://server.example.org/,coaps+tcp:// server.example.org/,coap+ws://server.example.org/
Lookup Request from client to RD
GET /rd-lookup/ep?ep=node1&tt=tcp
Res: 2.05 Content
<coap+tcp://server.example.org;ep="node1",
<coaps+tcp://server.example.org;ep="node1"