## Slide 1: CoAP Protocol Negotiation draft-silverajan-core-coap-protocol-negotiation Bill Silverajan Tampere Univ of Technology

## Slide 2: Background
Aimed at CoAP endpoints wishing for multiple transports and/or locations to exchange CoAP requests and responses
Transport availability falls into the following node categories
  Type T0 nodes have a single transport
  Type T1 nodes have 1 or more transports, which may be in unreachable/off states but at least 1 active transport
  Type T2 nodes have multiple active transports

## Slide 3: Why we need this (..and we do )
Enables client-side discovery of server transports
Reduces URI aliasing at origin server
Eliminates URI path complexity

## Slide 4: Allow Discovery
CoAP clients to discover active transports on an origin server
R1
Type T1
CoAP Server
SMS
UDP
Type T2
CoAP Client
UDP
SMS
Can I get resources over UDP?
Radio’s up, yes you can, here’s how
CoAP GET Request for R1
CoAP Response

## Slide 5: Avoid URI aliasing
Express same/related resource in alternate transports and locations
Type T2
CoAP Server
UDP
TCP
HTTP Client A
HTTP
HTTP Client B
HTTP
HTTP - CoAP Proxy
UDP
TCP
HTTP
R1
R1
R1 retrieved only once
coap/udp
coap/tcp
1. HTTP Client A to Proxy: Get me CoAP Server resource R1 over UDP
2. Proxy gets R1 from CoAP Server over UDP
3. HTTP Client B to Proxy: Get me CoAP Server resource R1 over TCP
4. Proxy to CoAP Server over UDP: Is it the same resource over TCP?
5. CoAP Server to Proxy over UDP: Yes, it is
6. Proxy Server returns cached R1 to HTTP Client B

## Slide 6: Reduce URI path complexity
Separate locator (endpoint subpath) from identifier (resource subpath)
  Example CoAP over WebSocket URI from earlier work (discarded owing to complexity):
  coap-at:ws://www.example.com/WebSocket?/sensors/temperature
WebSocket endpoint locator
CoAP resource Identifier

## Slide 7: Reduce URI path complexity
Separate locator (endpoint subpath) from identifier (resource subpath)
HTTP and
WS Client
WS
HTTP
R1
Type T2
CoAP Server
UDP
WS
HTTP - CoAP Proxy
UDP
HTTP
HTTP Client uses proxy to reach CoAP Server at UDP endpoint, server.example.com
HTTP Client solicits CoAP Server for WebSocket transport and endpoint info
CoAP Server responds giving WebSocket endpoint location as server.example.com/path/to/websocket
HTTP Client initiates WebSocket handshake with CoAP Server and negotiates CoAP subprotocol
Client switches to CoAP over WebSocket and retrieves resources from CoAP Server

## Slide 8: How can this be achieved?
Origin server simply exposes with .well-known/core:
  a new link attribute “tt” containing list of priority ordered transport types for coap and coaps resources
  a new link relation type “alt-loc” containing alternate endpoint locations (and not resource path)
REQ: GET /.well-known/core
RES: 2.05 Content </sensors>;ct=40;title="Sensor Index", tt="tcp ws sms”,
</sensors/temp>;rt="temperature-c";if="sensor”,
</sensors/light>;rt="light-lux";if="sensor”,
<coap+tcp://server.example.com/>;rel="altloc”,
<coap+tcp://server.example.net/>;rel="altloc”,
<coap+ws://server.example.com/ws-endpoint/>;rel="altloc”,
<coaps+sms://12147205269/>;rel="altloc"

## Slide 9: Next Steps to consider
Still lots of open work, contributions welcome!
Lifetime value for transport types?
Observe relationship to detect new / expired CoAP transports?
Is session continuity/resumption across new transports needed?
Support alt-loc for Type T0 (single transport) nodes too? (eg sleepy node, pub/sub support, etc)
Security considerations