## Slide 1: CoAP Protocol Negotiation draft-silverajan-core-coap-protocol-negotiation Bill Silverajan TUT Mert Ocak Ericsson

## Slide 2: Summary of changes from -02
Restructuring for easier editing
Scenarios and examples added
Node classification based on transport types
CoAP transports can have ”al” (active lifetime) attribute

## Slide 3: Forthcoming change: Usage of URI Templates
Change this operation:
  Client ----> GET /.well-known/core?tt=* ---> Server
  Client <--- 2.05 Content, tt="tcp sms” <--- Server
Into this operation:
  Client ---- GET /.well-known/core?rt=core.pn ----> Server
  Content-Format: application/link-format
  Client <-- 2.05 Content"</pn>;rt="core.pn";ct=40 <--- Server
Introduce a discovery interface for CoAP transports:
Method: GET
URI Template: /.well-known/core
URI Template: /{+pn}{?q*}
Example Request: GET /pn?tt="tcp"

## Slide 4: Proposal: Client-Initiated Transport Negotiation
In version -03, waking up an inactive transport is implicit:
  Client ----> GET coap+sms://0012345/.well-known/core?tt=udp ----> Server
  Client <--- 2.05 Content, <coap://example.org/>;rel_”altloc”;al=120 <-- Server
Work for version -04: New CoAP option
  For clients to request activating server’s inactive transport
  Prevent transport from going inactive (eg by extending lifetime)
Example 1:
  Client ----> GET coap+sms://001234567/pn?tt=udp ----> Server
  Client <--- 4.04 “Not Found” <-- Server
Example 2:
  Client ----> GET coap+sms://001234567/pn?tt=udp ----> Server
  OPTION ACTIVE_TRANSPORT
  Client <-- 2.05 Content <coaps://example.org/>;rel=”altloc”;al=120;tt=udp <-- Server
Alternatives to above approach?

## Slide 5: Session continuation
Mechanism for client to inform server to continue session over a different CoAP transport
  Many pitfalls envisaged (Observe, Block Transfers, switching to less secure channel)
Go/no-go decision to explore?